## Slide 1: Hydraulic Fracturing Regulatory Processes in Louisiana
1
James H. Welsh
Commissioner of Conservation

## Slide 2: Areas of Current & Potential Activity
Tuscaloosa Marine Shale
Haynesville Shale
BROWN DENSE

## Slide 3: Regulatory Goals
Resource Conservation / Sustainability
Waste Minimization
Pollution Prevention
Transparency
Awareness / Surveillance

## Slide 4: Regulatory Processes
  Water Source Management / Evaluation
  Work Permits
  Well Construction Requirements
  Waste Management / Disposal Requirements
  Fracturing Fluid Disclosure
  Inspection & Enforcement

## Slide 5: Water Sources – Surface Water
Use of surface water is encouraged.
Cooperative Endeavor Agreements may be created through DNR – Office of Mineral Resources (OMR) for the use of running surface water. (Act 955 of 2010)
Application process involves assessing the environmental/ecological impacts and economic benefits of surface water use.

## Slide 6: Water Sources – Ground Water
Notice is required prior to installation of new wells and prior to a change in use of existing wells for evaluation purposes.
Orders may be issued to collect information, conduct metering, impose well spacing requirements, or limit production.
Information may be used to establish areas of groundwater concern.

## Slide 7: Water Sources – Other
Certain E&P Wastes may be used as a frac fluid component in limited cases.
Promotes both waste minimization and resource conservation.

## Slide 8: Water Sources – Reporting
Water sources and volumes must be reported for wells that are hydraulically fractured.
Reporting is accomplished by filing Supplemental Page 3 of the Well History and Work Resumé Report (Form WH-1) following well completion.

## Slide 9
Water Use Statistics
Reported Usage from 10/1/2009 to 2/23/2012
Source | Volume (Gallons)
Frac Groundwater | 1,230,712,693
Frac Surface Water | 8,223,152,516
Drilling Rig Groundwater Supply | 879,649,632
Drilling Rig Surface Water Supply | 157,839,504
Other Groundwater | 155,545,829
Other Surface Water, | 39,007,638
Frac Stages | 22,338
Total Frac Water Used (gallons) | 9,453,865,209
Volume per Frac Stage (gallons) | 423,219
Average Frac Stages per Well | 11.4
Average Water Use per Well (gallons) | 5,454,777
Average Frac Water Use per Well (gallons) | 4,825,863
9
Water Usage Data for 1959 Haynesville Shale Natural Gas Wells
Chart: 
| Rig Supply Ground Water | Frac Supply Ground Water | Other Ground Water | Rig Supply Surface Water | Frac Supply Surface Water | Other Surface Water
 | 879649632 | 1230712693 | 155545829 | 157839504 | 8223152516 | 39007638

## Slide 10: Work Permits
A work permit application (Form DM-4R) must be approved prior to conducting fracturing operations.
Process allows for OC inspection of operations.

## Slide 11: Well Construction Requirements
  Use of multiple cemented casing strings
  Minimum setting depth to protect USDW
  Post-installation pressure testing

## Slide 12: Waste Management
E&P Waste regulations ensure proper disposal to minimize environmental impacts of resource development.
Manifest and reporting systems ensure transparency and accountability.
Waste Management options include:
  Onsite disposal
  Well injection
  Commercial disposal
  Recycling in limited cases

## Slide 14: Fracturing Fluid Disclosure
  Types and volumes (in gal.) of hydraulic fracturing fluid
  List of additives used
  List of chemical ingredients subject to requirements of 29 CFR 1910.1200(g)(2)
  Maximum ingredient concentration within the additive
  Ingredients and concentrations of proprietary chemicals are not required.
  Required information may be reported to Frac Focus website.

## Slide 15: Fracturing Fluid Disclosure Requirements by State

## Slide 16: Inspection & Rule Enforcement
Periodic visual inspections of wells are conducted during all phases of development
Regulatory violations result in the issuance of Compliance Orders to the responsible party requiring corrective actions.
Possible enforcement actions include
  Levy of Civil Penalties
  Suspension of authority to sell oil
  Withholding permits
  “Orphaning” Declaration

## Slide 17: STRONGER Review
STRONGER, Inc. is a nonprofit multi-stakeholder organization which measures state oil and gas waste management programs against a set of Guidelines developed and agreed to by all the participating parties.
A Louisiana Review focusing on hydraulic fracturing regulatory practices was conducted in November 2010; Findings were issued in March 2011.
Positive Assessments of Louisiana’s Regulatory Framework:
  Proactive conservation of groundwater resource use.
  Waste water recycling program.
  Public outreach and education.
  Waste disposal regulations.
Areas for Improvement:
  Updated Casing and Cementing Requirements. (IN PROGRESS)
  More systematic training of Inspectors. (IN PROGRESS)
  Require the reporting of hydraulic fracturing information including component constituents of frac fluid. (COMPLETED)

## Slide 18: Potential Future Rule Changes
Frac Fluid Disclosure
  Disclosure requirements tied to “Right to Know” federal law instead of OSHA safety communication rules.
Casing and Cementing
  Clear design objectives
  Formation Integrity Tests
  Cement evaluation following prolonged drilling
  Liner seal testing
  Cement top verification in limited circumstances